## Slide 1: Ch 1 Internet Protocol Overview
TCP/IP and the IP Layer overview

## Slide 2: Internet Protocol
a set of rules governing the format of data sent over the Internet or other network.
IP, as the primary protocol in the Internet layer of the Internet protocol suite, has the task of delivering packets from the source host to the destination host solely based on the IP addresses in the packet headers.
For this purpose, IP defines packet structures that encapsulate the data to be delivered. It also defines addressing methods that are used to label the datagram with source and destination information.

## Slide 3: TCP/IP
It is commonly known as TCP/IP, because its most important protocols, the Transmission Control Protocol (TCP) and the Internet Protocol (IP), were the first networking protocols defined in this standard
TCP/IP provides end-to-end connectivity specifying how data should be packetized, addressed, transmitted, routed and received at the destination. This functionality is organized into four abstraction layers which are used to sort all related protocols according to the scope of networking involved

## Slide 4: Why Communications Architecture
The complexity of the communication task is reduced by using multiple protocol layers:
    Each protocol is implemented independently
    Each protocol is responsible for a specific subtask
    Protocols are grouped in a hierarchy
A structured set of protocols is called a communications architecture or protocol suite

## Slide 5: Who Built TCP/IP?
Internet Architecture Board (IAB)
Originally known as Internet Activities Board
Evolved from Internet Research Group
Forum for exchange among researchers
About a dozen members
Reorganized in 1989 and 1993
Merged into the Internet Society in 1992

## Slide 6: TCP/IP Protocol Suite
The TCP/IP protocol suite is the protocol architecture of the Internet
The TCP/IP suite has four layers: Application, Transport, Network, and Data Link Layer
End systems (hosts) implement all four layers. Gateways (Routers) only have the bottom two layers.

## Slide 7: Functions of the Layers
Data Link Layer:
  Service: Reliable transfer of frames over a link Media Access Control on a LAN
  Functions: Framing, media access control, error checking
Network Layer:
  Service: Move packets from source host to destination host
  Functions: Routing, addressing
Transport Layer:
  Service: Delivery of data between hosts
  Functions: Connection establishment/termination, error control, flow control
Application Layer:
  Service: Application specific (delivery of email, retrieval of HTML documents, reliable transfer of file)
  Functions: Application specific

## Slide 8: TCP/IP Suite and OSI Reference Model
The TCP/IP protocol stack does not define the lower layers of a complete protocol stack

## Slide 9: Assignment of Protocols to Layers
Routing Information
Protocol
Protocol Independent
Multicast
Open Shortest Path First
Simple Network Management Protocol

## Slide 10: Layered Communications
An entity of a particular layer can only communicate with:
  1. a peer layer entity using a common protocol (Peer Protocol)
  2. adjacent layers to provide services and to receive services

## Slide 11: Layers in the Example