## Slide 1: Chapter 2
IPv4 and IPv6 Address Types and Formats

## Slide 2: What is an IP Address
An Internet Protocol address (IP address) is a numerical label assigned to each device (e.g., computer, printer) participating in a computer network that uses the Internet Protocol for communication
An IP address serves two principal functions: host or network interface identification and location addressing.
Its role has been characterized as follows:
  A name indicates what we seek.
  An address indicates where it is.
  A route indicates how to get there

## Slide 3: Contd..
IP addresses are binary numbers, but they are usually stored in text files and displayed in human-readable notations, such as 172.16.254.1 (for IPv4)
The Internet Assigned Numbers Authority (IANA) manages the IP address space allocations globally and delegates five regional Internet registries (RIRs) to allocate IP address blocks to local Internet registries

## Slide 4: Type of Address
Public IP Address
Public IP addresses are those that allow any two computers to identify each other.
When a person connects to the Internet, his/her computer is usually assigned an address from a pool that has been set aside for her Internet Service Provider (ISP) to use for its customers
Most of the addresses in the IPv4 host range are public addresses.
These addresses are designed for used by hosts that are publicly accessible from the Internet.
Even within these address blocks, there are many addresses that are designated for other special purposes

## Slide 5: Contd….
Private Addresses
When several computers or devices are connected to each other, either with cables or wirelessly, they can make up a private network.
Each device within this network is assigned a different IP address in order to exchange files and share resources within the network
Although addresses must be unique within the private network, different private networks could all use the same addresses
The router or firewall within the network is assigned a public IP address by the Internet Service Provider (ISP); this single public IP address identifies the entire network on the Internet
Using a built--‐in device called a Network Address Translator (NAT), the router acts as a gatekeeper and passes requests from individual computer users to the Internet

## Slide 6: Internet Protocol Version 4 (IPv4)
IPv4 addresses are canonically represented in dot-decimal notation, which consists of four decimal numbers, each ranging from 0 to 255, separated by dots, e.g., 172.16.254.1. Each part represents a group of 8 bits (octet) of the address.
IPv4 is the fourth version in the development of the Internet Protocol and is described in IETF publication RFC 791
IPv4 is a connectionless protocol for use on packet-switched networks. It operates on a best effort delivery model, in that it does not guarantee delivery, nor does it assure proper sequencing or avoidance of duplicate delivery

## Slide 7: Addressing
IPv4 uses 32-bit (four-byte) addresses, which limits the address space to 4294967296 (232) addresses. As addresses were assigned to users, the number of unassigned addresses decreased
IPv4 reserves special address blocks for private networks (~18 million addresses) and multicast addresses (~270 million addresses)
IP Address consist two Portion: Network number portion and Host number portion
There are four forms of IP addressing, each with its own unique properties.
  Unicast :one to one
  Broadcast: one to all possible host
  Multicast: one to Interested group
  Anycast: one to many (Decide by Router, Used in IPv6)

## Slide 8: Internet Protocol Version 6 (IPv6)
IPv6 is the Internet‘s next--‐generation protocol, designed to replace the current Internet Protocol, IP Version 4.
IPv6 is a standard developed by the Internet Engineering Task Force, an organization that develops Internet technologies.
The IETF, anticipating the need for more IP addresses, created IPv6 to accommodate the growing number of users and devices accessing the Internet
IPv6 addresses are 128 bits, which allow for approximately three hundred and forty trillion, trillion unique IP addresses. An example IPv6 address is: 2001:db8:ffff:1:201:02ff:fe03:0405