## Slide 1: Unit 3
Broadband Communications,
Policy, xDSL and Cable Internet

## Slide 2: Broadband Communications
A transmission facility having a bandwidth sufficient to carry multiple voice, video or data channels simultaneously. Each channel occupies (is modulated to) a different frequency bandwidth on the transmission medium and is demodulated to its original frequency at the receiving end; NB used originally to describe a channel with more bandwidth than a standard 48 KHz voice grade channel.
Broadband refers to telecommunication in which a wide band of frequencies is available to transmit information.
Because a wide band of frequencies is available, information can be multiplexed and sent on many different frequencies or channels within the band concurrently, allowing more information to be transmitted in a given amount of time (much as more lanes on a highway allow more cars to travel on it at the same time).
It is generally agreed that Digital Subscriber Line (DSL) and cable TV are broadband services in the downstream direction.
Related terms are wideband (a synonym), baseband (a one-channel band), and narrowband (sometimes meaning just wide enough to carry voice, or simply "not broadband").

## Slide 3: Contd..
At present, there is no internationally agreed definition of broadband.
In general, broadband often refers to internet access service with transmission speed from hundreds of kbps (kilobits per second) to several Mbps (Megabits per second)
Note that 'dedicated bandwidth' or 'shared bandwidth' services advertised by ISPs normally refers to the transmission speed of the customer access circuit between the customer's premise and the nearest exchange.
The active users still have to share the public network resources outside the exchange, including local and external transmission circuit

## Slide 4: Flavours of Broadband Communications
Fibre optics
  Fibre to the home?
DSL/Cable Modems
  Data rates cost etc
Wireless
  IEEE802.11
Mobile
  3G and beyond

## Slide 5: Broadband Policy of Nepal
The Broadband Policy is considered to be key to development of information and communication technology and implementation of e- governance. I
t is expected to make service delivery easy and effective in remote area by expanding wireless broadband internet as other means of communication are difficult because of rough terrain.
The term broadband has not yet been defined in the context of Nepal even though it has been 15 years since the Internet became available in the country.
The broadband policy is crucial for the overall development of the information and communication technology sector.
According to the draft policy, broad band will identify. The minimum speed in kbps- uplink and downlink- where ever the service is offered.
It will also guarantee the quality of service throughout on a shared or dedicated basis on services that a service provider offers.
At present, broadband has nothing to do with speed or quality. Currently local Internet service provider are advertising their services as broadband Internet without knowing its standards.

## Slide 6: xDSL
Digital subscriber line (DSL; originally digital subscriber loop) is a family of technologies that are used to provide internet access by transmitting digital data over telephone lines.
xDSL Refers collectively to all types of digital subscriber lines, the two main categories being ADSL and SDSL. Two other types of xDSL technologies are High-data-rate DSL (HDSL) and Very high DSL (VDSL)
DSL technologies use sophisticated modulation schemes to pack data onto copper wires. They are sometimes referred to as last-mile technologies because they are used only for connections from a telephone switching station to a home or office, not between switching stations
In telecommunications marketing, the term DSL is widely understood to mean asymmetric digital subscriber line (ADSL), the most commonly installed DSL technology. DSL service is delivered simultaneously with wired telephone service on the same telephone line, this is possible because DSL uses higher frequency bands for data.
On the customer premises, a DSL filter on each non-DSL outlet blocks any high-frequency interference to enable simultaneous use of the voice and DSL services

## Slide 7: Types of DSL
ADSL - (Asymmetric Digital Subscriber Line) is the most popular form of DSL technology.
ADSL Lite - A lower data rate version of Asymmetric Digital Subscriber Line (ADSL)
CDSL - Consumer Digital Subscriber Line (CDSL) is a proprietary technology trademarked by Rockwell International.
Ether Loop – Ether Loop is currently a proprietary technology from Nortel, short for Ethernet Local Loop.
HDSL - High Bit-rate Digital Subscriber Line (HDSL) is generally used as a substitute for T1/E1.
IDSL - ISDN based DSL developed originally by Ascend Communications.
RADSL - Rate Adaptive Digital Subscriber Line (RADSL) is any rate adaptive DSL modem, but may specifically refer to a proprietary modulation standard designed by Globe span Semiconductor.
SDSL - Symmetric Digital Subscriber Line (SDSL) is a 2-wire implementation of (HDSL).
VDSL - Very High Bit-rate Digital Subscriber Line (VDSL) is proposed for shorter local loops, perhaps up to 3000 ft.

## Slide 8: Cable Internet
In telecommunications, cable Internet access, shortened to cable Internet is a form of broadband Internet access that uses the cable television infrastructure.
Like digital subscriber line and fiber to the premises services, cable Internet access provides network edge connectivity (last mile access) from the Internet service provider to an end user.
It is integrated into the cable television infrastructure analogously to DSL which uses the existing telephone network.
Cable TV networks and telecommunications networks are the two predominant forms of residential Internet access. Recently, both have seen increased competition from fiber deployments, wireless, and mobile networks.
Broadband cable Internet access requires a cable modem at the customer's premises and a cable modem termination system at a cable operator facility, typically a cable television headed.
The two are connected via coaxial cable or a Hybrid Fiber Coaxial (HFC) plant.

## Slide 9: Contd..
While access networks are sometimes referred to as last-mile technologies, cable Internet systems can typically operate where the distance between the modem and the termination system is up to 160 kilometers (99 mi).
If the HFC network is large, the cable modem termination system can be grouped into hubs for efficient management.
Downstream, the direction toward the user, bit rates can be as much as 400 Mbit/s for business connections, and 250 Mbit/s for residential service in some countries. Upstream traffic, originating at the user, ranges from 384 kbit/s to more than 20 Mbit/s.
One downstream channel can handle hundreds of cable modems. As the system grows, the cable modem termination system (CMTS) can be upgraded with more downstream and upstream ports, and grouped into hubs CMTS for efficient management.
Most Data Over Cable Service Interface Specification (DOCSIS) cable modems restrict upload and download rates, with customizable limits.
These limits are set in configuration files which are downloaded to the modem using the Trivial File Transfer Protocol, when the modem first establishes a connection to the provider's equipment.
Some users have attempted to override the bandwidth cap and gain access to the full bandwidth of the system (often as much as 30 Mbit/s), by uploading their own configuration file to the cable modem - a process called uncapping.

## Slide 10: How Cable Internet Works
Unlike dial up and DSL, which transmit data over a phone line, cable Internet service uses the cable TV infrastructure to transmit data.
Cable Internet users have a special cable modem, provided by the cable Internet companies themselves that use a slice of the available bandwidth of the connection to download an upload information.
Just like how a DSL connection does nit tie up its phone line, a cable Internet connection does not affect the ability to watch TV throughout the house
Benefits of Cable High speed
Speed- Cable Connections are incredibly quick, with some cable Internet provider able to deliver download speeds as fast as 100 mbps.
Consistency- While the speed of a DSL connection is based on how close your house is to the phone company, cable connection will have a consistent speed no matter how far away the cable company is
No Landline Required- A cable connection does not require a phone line, which can help save your money
Price – Cable high speed service typically delivers the lowest cost per Mbps in given area
Always on Unlike a dial up connection, a cable connection is constantly connected and ready whenever you are