## Slide 1: Unit 4
VoIP, GoIP and IP Interconnection

## Slide 2: Introduction: VoIP
VoIP is an acronym for Voice Over Internet Protocol, or in more common terms phone service over the Internet.
VoIP is a technology that allows telephone calls to be made over computer networks like the Internet. VoIP converts analog voice signals into digital data packets and supports real-time, two-way transmission of conversations using Internet Protocol (IP)
Voice over IP (VoIP) is a methodology and group of technologies for the delivery of voice communications and multimedia sessions over Internet Protocol (IP) networks, such as the Internet. Other terms commonly associated with VoIP are IP telephony, Internet telephony, broadband telephony, and broadband phone service.
If you have a reasonable quality Internet connection you can get phone service delivered through your Internet connection instead of from your local phone company
VoIP calls can be made on the Internet using a VoIP service provider and standard computer audio systems. Alternatively, some service providers support VoIP through ordinary telephones that use special adapters to connect to a home computer network. Many VoIP implementations are based on the H.323 technology standard

## Slide 3: Contd..
VoIP services that utilize existing broadband Internet access, by which subscribers place and receive telephone calls in much the same manner as they would via the public switched telephone network (PSTN).
A VoIP phone is necessary to connect to a VoIP service provider. This can be implemented in several ways:
  Dedicated VoIP phones connect directly to the IP network using technologies such as wired Ethernet or Wi-Fi. They are typically designed in the style of traditional digital business telephones.
  An analog telephone adapter is a device that connects to the network and implements the electronics and firmware to operate a conventional analog telephone attached through a modular phone jack. Some residential Internet gateways and cablemodems have this function built in.
  A softphone is application software installed on a networked computer that is equipped with a microphone and speaker, or headset.
VoIP offers a substantial cost savings over traditional long distance telephone calls.
The main disadvantage of VoIP is a greater potential for dropped calls and degraded voice quality when the underlying network links are under heavy load

## Slide 4: Introduction: GoIP
The GoIP series gateway is a broadband relay gateway newly developed by DBL Technology.
It is a new product for seamless connection between the GSM network and VoIP network.
When the mobile phone SIM card is installed in the GoIP, users can register the GSM phone to the VoIP softswitch system.
In addition, the GoIP supports the transparent transmission of the caller number from the PSTN to the VoIP.
GoIP is designed to work in conjunction with key phone systems and IP-PBX to provide GSM communications.
GoIP is a great way to provide fast phone service deployment where regular PSTN line may not be readily available.
The GoIP features embedded SIP and H.323 protocols with flexible setting.
The bi-directional password authentication (call authorization) and trust list authentication greatly minimize the risk of charge losses and the flexible routing function can meet special requirements of various call forwarding.
With its low price, excellent voice quality, and powerful features, the GoIP series gateway is the first choice for system integrators, traffic operators, and softswitch manufacturers.

## Slide 5: Usage concept
Sim-card is put into GSM-gateways (or SIM-bank connected to GSM-gateway) in order to register it in GSM network, at the same time the gateway is connected with VoIP through program switch.
Accordingly the traffic can be converted in and out between GSM and VoIP channels.
SIP(Session Initiation Protocol) and H.323 protocols are used for media traffic termination.
In compare with PSTN, GSM-gateways provides drastic economy by amending the infrastructure and lowering the expenditures on technical support.
GoIP includes an integral support of SIP and H.323 protocols with flexible settings.
Duplex authentification of password and trust-list back-up will significantly decrease the risk of getting huge bills for telecommunication, besides it maintains an adaptable system of call transfer.

## Slide 6: Application of GoIP
Call Forward
  Call Origination refers to a call initiated from the PSTN or cell phone network is terminated using VoIP.
  Call Termination refers to a call initiated as a VoIP call is terminated using PSTN or cell phone network.
IP PBX Call Origination and Termination
  VoIP endpoints connected to the IP PBX can make calls to cellular/traditional telephone network via the GoIP GSM ports.
  Outside callers can then call in via the GoIP GSM ports to reach any of the VoIP endpoints that are registered to the IP PBX.
  GoIP can be configured in a group mode such that all GSM ports can be used by just dialing only one GSM number. Please refer to the Call Center Application for more information.

## Slide 7: Contd..
Sending Bulk SMS Service
  Sending bulk sms text messages is a common technique for telemarketing to reach the target customers.
  A bulk SMS system can be implemented quickly and easily using GoIPs and our proprietary SMS server. Telemarketers are now have full control on how and when they want to send text messages.
  SMS text messages are now used widely in many companies, organizations, schools, clubs as a mean for broadcasting information. They can now build their own SMS system without paying expensive charges to their GSM server provider.
  This system can also take the advantage of using the same GSM service provider to send sms to the phone subscribers in the same service provider.
Call Back
  Call Back is referring to the telecommunications event that occurs when the originator of a call is immediately called back in a second call as a response.
  GoIP could be used to achieve this function alone or as an terminal that is integrated in an existing call back server / platform.

## Slide 8: Competitive Advantage:
Remote SIM operation for SIM Card management
SMPP support for 3rd party development of SMS Applications.
Free server utilities for remote access and SMS management.
Telnet mode for sending AT commands to GSM module.
Compact and light weight design
Direct customer support